Mercury 7

Handheld Magnification & OCR

Support Email: support@issist.com

www.issist.com

Table of Contents

Getting it to Work	5

Zoom	7

Background Color of reading text	7

Reading in Low light	7

OCR for Self Reading	8

- Enabling/Disabling Table Mode……………………………………………………8

Saving Text Image	10

Viewing saved Images for OCR	10

Changing the relevant settings	11

Table of Figures

Figure 1: Live Magnification	6

Figure 2: Zooming In & Out	7

Figure 3: Changing Text Background Color	7

Figure 5: Starting OCR	8

Figure 6: Taking Image	8

Figure 7: Image Processing	9

Figure 8: Saving Image	9

Figure 9: View Saved Image	9

Figure 10: Manipulating Image	10

Figure 11: Changing Settings	11

Figure 12: Setting Options	12

Figure 13: Close current screen	14

IMP: DO NOT PRESS THE POWER BUTTON AND VOLUME BUTTON AT THE SAME TIME

If you do press the buttons together you will be directed to Factory reset. Please follow instructions on how to reset the unit on page 17 .

Mercury 7  is a  Hanheld device with

- built-in 7’’ touch screen

- USB Charger

- an integrated volume button & a port for connecting headphone.

# Getting it to Work

Press the Power button on the right to start your unit. After 10 seconds you will hear a boot up tune and see the issist logo.

Mercury comes with a built in stand. Open the stand to stabilize the unit during live magnification-

The unit will start up in live magnification mode. If you’re handheld doesn’t start please plug in the charger provided & charge the unit.

You will see a battery sign come up. It will indicate the battery level. Please charge your unit before switching it on. Press down for 3 seconds to start live magnification.

Live Magnification Mode

Touch with one finger to focus.

Figure 1: Live Magnification. One finger touch

# Zoom

For Zooming In & Out, use the ‘Pinch and stretch’ action.

Figure 2: Zooming In & Out

You can always move around the text areas to focus on your desired part.

# Background Color of reading text

Taping the screen with three fingers will change the background color of the text.

Figure 3: Changing Text Background Color- Three finger touch

# Reading in Low light

It has a built-in light for reading in dim places. To switch on & off the light, touch with four fingers. It will give a voice notification on light off & on.

OCR for Self Reading

Tap on the red circle on the top left side twice to go into reading mode

Figure 4: Starting OCR

After taping the button, a new interface comes up in a moment. This will be something similar to the following.

Figure 5: Taking Image

To take an image of the text tap the grey shaded camera icon twice.

Enabling/Disabling table mode (we recommend keeping table mode enabled)

Table mode identifies tables and reads text within the table, table mode is recommended for invoices, Waybills, Magazines. Table mode can be disabled when you need to read all text horizontally. Tap on the TABLE button to enable and disable table mode

Original Mode & Wrapped Mode

Original Mode                                                          Wrapped Mode

In original mode the original picture will be displayed. Pinch to zoom in and out, tap on any word to forward rewind.

In the wrapped mode text will be reformatted as shown above. Pinch to zoom in and out, use the buttons given to pause forward and rewind.

Once the mode is set tap in the middle to take a picture

Figure 6: Image Processing

It takes the image instantly and starts processing the image for reading itself as per earlier defined voice settings. Tap on the X button on the top left to exit out of the processing

## Saving Text Image

To save an image of the text for future OCR/self-reading, we need to tap the green circle icon on the bottom left.

Figure 7: Saving Image

## Viewing saved Images for OCR

Saved images can be viewed by taping the bottom right circle icon.

Figure 8: View Saved Image

After taping the icon, the image(s) appear on the screen date & time wise.

Figure 9: Manipulating Image

For self-reading of the shown image on the screen, we need to tap the screen two times very quickly. It starts the processing and starts reading. To stop reading just tap the ‘X’ icon on the top left of the screen while reading is going on.

# Changing the relevant settings

Figure 10: Changing Settings

Taping the settings icon twice opens the screen below –

Figure 11: Setting Options

General Settings: This setting influences both the Reading mode and the Magnification mode.

*Tap twice to select an option. When you press on the exit button your choice will be implemented

Orientation: Select the orientation of the displayed screen

Selection: Choose between the option of double tap or single tap for choosing any item

Under General Settings you can set the following options

- Speech Options has options for

  - Changing Rate – to set Low, Medium & High rate of speaking voice.

  - Volume – to set Low, Medium & High volume level of the auto speaker.

  - Voice style – to set voice style accent.

- Text Options has options for

  - Text Size – to change the visual size of the font in to Small, Medium & Large.

  - Text Color – to change the color of the text in to Original, White, Black, Blue & Red.

  - Highlight Color– to change the color in to White, Black, Blue, Red & Yellow.

  - Background Color– to change the color in to Original, White, Black, Blue & Red.

Language Options: English or other

Orientation: This rotates the screen 180 degrees

Reader Setting: This changes the settings in the reading mode

Reading Mode has options for

  - Original- This mode highlights and reads text on the original picture taken

  - Wrapped- This mode reformats text in one boxed area and makes it easy to scroll

- Camera has options for selecting from Integrated Camera or USB Camera

- Image Enhancement: The default is Off

To change the text color in Reading mode select ‘On’ under Image Enhancement. The text in reading mode will now be enhanced to the color selected by you.

Magnifier Settings: This changes the settings in the magnification mode.

User can set the Minimum Zoom level to 1X

We can navigate & close settings by taping the red ‘X’ on the screen anytime we like. Tapping on the X implements the changes made.

*If you press the power and volume button when starting your device and it locks.

Please take out the battery from the back of the unit and put it back again to restart the unit.

To watch video instructions and learn more please visit us - http://issist1.com/?page_id=935

# Text boxes

Image Navigation

Delete the current image

Open the Settings

Toggle the Light

Figure 12: Close current screen

Tap twice to go into reading mode

Tap twice on settings to go into settings

Tap in the middle twice to take a picture and read it

Load Mode – You can view all your saved pictures in this mode. Pictures are saved date wise

Press the save button to save pictures

Press the X button on the top left to stop processing

DO NOT PRESS VOLUME AND POWER BUTTON AT THE SAME TIME

Integrated stand for live magnification

Power Button

Change color while reading

Picture can be saved while reading

Camera

For distance capture. Take a picture and zoom in

Table mode identifies tables and reads text within the table. Tap on the icon twice to enable & disable table mode