## Attaching your BuzzClip to a White Cane

The cane attachment is the newest feature in the latest generation of the BuzzClip. You will find the attachment in your box and attach it to the back/bottom part of your BuzzClip when using it in conjunction with a white cane.

When sliding in the cane attachment to your BuzzClip ensure that you are holding the attachment and your BuzzClip vertically and parallel to each other. Slide your BuzzClip from above into the allotted area on your attachment to lock it in place. You can then tilt it up or down to face it below or above waist level to cater to your personal mobility needs.

For example, you can tilt it downwards to allow detection of obstacles on the ground that a white cane may not detect or tilt it upwards to allow for protection above the waist, especially at the head level.

## Using your BuzzClip

The BuzzClip is not a replacement for a cane but a complementary mobility tool. It is intended to be used in combination with a cane or a guide dog. For those who frequently travel with a cane or a guide dog, we recommend using the BuzzClip to address upper body and head level obstacles while the cane can address changes in elevation and lower obstacles. The BuzzClip can also be used on its own when in familiar indoor environments and for people living with partial sight who do not use a cane or a guide dog.